## Slide 1: Error Mitigation and Randomized Benchmarking for Quantum Circuits
Rajesh Sathya Kumar

## Slide 2: Error Mitigation for NISQ
The Long-term plan in Quantum industry is to design a fault tolerant error corrected Quantum Computers. However, the various error mitigation techniques are developed in the meantime to make use of these NISQ era Quantum Computers for real world applications

## Slide 3: Zero Noise Extrapolation (ZNE)
The ZNE method works by assuming that the amount of noise present when a circuit is run on a noisy device is enumerated by a parameter g. Suppose we have an input circuit that experiences an amount of noise g = g0 when executed. Ideally, we would like to evaluate the result of the circuit in the g = 0 noise-free setting.
To do this, we create a family of equivalent circuits whose ideal noise-free value is the same as our input circuit. However, when run on a noisy device, each circuit experiences an amount of noise g = s * g0 for some scale factor s≥1. By evaluating the noisy outputs of each circuit, we can extrapolate to s=0 to estimate the result of running a noise-free circuit.

## Slide 4: Unitary Folding
When the scale factor is s=1, the resulting circuit is
V=U†U=I.
Hence, the s=1 setting gives us the original unfolded circuit.
When s=3, the resulting circuit is
VV†V=U†UUU†U†U=I.
In other words, we fold the whole circuit once when =3. Generally, whenever ss is an odd integer, we fold (s−1)/2 times.
The s=2 setting is a bit more subtle. Now we apply folding only to the second half of the circuit, which is in our case given by U†. The resulting partially-folded circuit is
(U†UU†)U=I

## Slide 5: Noise Scaling Factor vs Expectation Value

## Slide 6: Intro to Randomized Benchmarking Protocol
Clifford Gates: In quantum computing, the Clifford Group is a set of gates defined by the property that they always transform Pauli’s to Pauli’s. Step 1: Generate RB sequences
Step 2: Execute the RB sequences (with some noise) Step 3: Get statistics about the survival probabilities Step 4: Find the averaged sequence fidelity Step 5: Fit the results

## Slide 7: References
T. Proctor, K. Rudinger, K. Young, E. Nielsen, R. Blume-Kohout “Measuring the Capabilities of Quantum Computers”, arXiv:2008.11294 (2020).
K. Temme, S. Bravyi, J. M. Gambetta “Error Mitigation for Short-Depth Quantum Circuits”, Phys. Rev. Lett. 119, 180509 (2017).
Y. Li, S. C. Benjamin “Efficient Variational Quantum Simulator Incorporating Active Error Minimization”, Phys. Rev. X 7, 021050 (2017).
T. Giurgica-Tiron, Y. Hindy, R. LaRose, A. Mari, W. J. Zeng “Digital zero noise extrapolation for quantum error mitigation”, IEEE International Conference on Quantum Computing and Engineering (2020).

## Slide 8: Plans next week
Explore more error mitigation methods
Simulation and getting performance of Quantum algorithms after error mitigation